## Slide 1
ELECTRICAL MACHINES

## Slide 2
Types of Electrical Machines.
DC MACHINES
Shunt, series, separately and compound excited,
Brush PM
INDUCTION (ASYNCHRONOUS) MACHINES
Capacitor start (single phase, squirrel cage)
Shaded-pole (single phase, squirrel cage)
3 phase squirrel-cage
3 phase wound-rotor (or slip-ring)
SYNCHRONOUS MACHINES
3 phase conventional excitation
3 phase Brushless Permanent (PM) Magnet
SPECIAL ELECTRICAL MOTORS
Reluctance motors, Stepper motor, Universal motors……

## Slide 3
How they work
Two electromagnetic conversion phenomena:
Induced voltage: when a conductor moves in a magnetic field, voltage is induced in the conductor. (Generator action)
Force and developed torque: when a current-carrying conductor is placed in a magnetic field, the conductor experiences a mechanical force. (Motor action)

## Slide 4: Rotating Electrical Machines
Fixed stator: This (normally) sets up magnetic field.
Rotating rotor: This (normally) carries currents (either supplied from a power source or (induced).
B
F
Current (I) flows in rotor.
Force on conductor: F=IBl
Torque: T=Fr
l
B
l
r
Stator sets up B field
Rotor
Stator

## Slide 5
Rotor rotates (anticlockwise)
1/4 revolution later we have
For a particular machine:
  How B is produced?
  How do we get currents in rotor to produce continuous torque?

## Slide 6: Principle of Operation of DC Motors
If
Field winding (2 coils in series as shown) carries field current If
If sets up magnetic field shape as shown
B

## Slide 7
ia
B
F
F
B
ia
Rotor carries “armature” winding.
Armature current ia fed to through commutator and brushes.
This feeds ia to different windings as rotor rotates. Result is that the current distribution in space is fixed.
Force = iaB.l always in direction shown since current distribution is fixed in space.
Torque = Force x radius
Torque = ia B.l r
F
B
i
Brush

## Slide 8
Commutators
Armature windings
Magnetic Core
Brushes
Permanent Magnet DC Motor

## Slide 9
F = I B l
l = length of conductor in field
1. Force on conductor carrying I in field B
F
B
i
i
B
F
e = B l
e = voltage induced along length l
2. Voltage (emf) induced in conductor traveling in field B
v
B
e
B
v
e

## Slide 10
  e induced in each conductor
  N conductors are all in series
  Therefore total "back-emf " induced
in armature winding is E = Ne
  E = N B l
 = r ( = angular velocity, rad/s)
E = Nr Bl = k
  E is proportional to 

F
F
ia

E

E
Vf
Va
ia
if
Rf
Ra
T, 
Equivalent circuit of a separately excited DC motor

## Slide 11
Winding Axis of Rotor
Note it is perpendicular to the magnet flux
Cross section of a permanent magnet DC motor
Direction of B
Rotor with Commutator and End Frame with Brushes of Simple Permanent Magnet Machine
Stator

## Slide 12: Characteristics of DC Machine
If sets field B. This normally constant
Torque = k if ia. If ia supplied form separate supply then ia controls torque. (If we want more torque then we inject more ia)
Carbon brushes required – sparking is common and brushes wear out – regular maintenance
Quite expensive due to commutator and armature winding construction.
Very common for small motors (tape recorders, CDs, drills, printers, photocopiers etc. In these cases, B is often supplied by a permanent magnet.
Can put armature and field winding in series and run it directly off single phase household mains. This called a “universal motor”. Used in lawn mowers, washing machines, cheap tools, hairdryers etc.

## Slide 13: Torque in Universal Motor
F
ia
B
ia = if maximum positive
ia = if
The single phase Universal Motor is very similar to a DC series motor. It can operate on either AC or DC and the resulting torque is about the same in each case. That is why it is called Universal Motor

## Slide 14
ia = if
ia = if zero
ia = 0
If = 0
F
ia
B
ia = if
ia = if maximum negative
Torque is pulsating
Torque

## Slide 15
Normally Universal motors are rated at fractional horse power (less than 1kW)
The main advantage of Universal motors is their high speed ( 1500 to 15000rpm) and high starting torque
Therefore, they are used to drive high speed centrifugal blowers in vacuum cleaners
The high speed and corresponding small size for a given power output is also an advantage in driving portable tools, such as electric saws and drilles
Characteristics of Universal Motor

## Slide 16: THE 3-PHASE INDUCTION MACHINE
 65% of world's generated energy  rotating machines
>90% of this  induction machines
Induction motor construction:
The induction motor comprises two parts:
outer stationary frame called the “stator”
inner rotating section known as the “rotor”
The stator has a large number of circular silicon steel laminations with slots cut in their inner circumference mounted in a fabricated or cast steel frame. Three phase windings mutually displaced by 120 in space are wound in the slots.

## Slide 17
Stator construction
  Laminated iron core with slots
  Coils are placed in the slots to form a three or single phase winding
Constructions and Types
The two principal parts of the motor are the rotor and the stator.
Squirrel-cage rotor construction
  Laminated Iron core with slots
  Metal bars are molded in the slots
  Two rings short circuits the bars
  The bars are slanted to reduce noise and harmonics

## Slide 18
Stator construction
  Laminated iron core with slots
  Coils are placed in the slots to form a three or single phase winding
Constructions and Types
The two principal parts of the motor are the rotor and the stator.
Squirrel-cage rotor construction
  Laminated Iron core with slots
  Metal bars are molded in the slots
  Two rings short circuits the bars
  The bars are slanted to reduce noise and harmonics

## Slide 19
The most common form of rotor known as the “squirrel cage rotor” It has silicon steel laminations keyed to a central shaft. Slots in the laminations at or close to the outer circumference, carry aluminium or copper conductors. The ends of the conductors are welded to aluminium end rings, which are sometimes castellated to facilitate cooling during operation
Stator
Rotor

## Slide 20
Power Range
200-500W small fans
1-50kW fans, pumps, conveyors, escalators
50-500kW water pumping, coal cutting,
1MW high speed train motor (eg. x4)
10MW warship/cruise liner motor (x2)
Iron
Al bars
End rings
Rotor
(side view)

## Slide 21
3 Phase Stator Winding

## Slide 22
Rotor Showing Single Bars Short Circuited by ‘End Rings’

## Slide 23: How Magnetic Field B is Produced
Representation of 3 stator windings
A
B’
C
B
C’
A’
3 phase windings on stator
A
B’
C
B
C’
A’
Principle of rotating field set up by 3-phase windings
B’
B
C
C’
Field due to AA’ winding
Due to BB’ winding
Due to CC’ winding
A
A'


## Slide 24
Red vector is voltage (or current or flux) due to phase A
Blue/Green vector for phase B and C respectively
Add blue and red together
Note resultant is 1.5 times peak of phase vector
Now, add in green vector
t1>t0
Initial
time t0
t2>t1
t3>t2
t4>t3
t1>t0
Initial
time t0
t2>t1
t3>t2
t4>t3
t1>t0
Initial
time t0
t2>t1
t3>t2
t4>t3

## Slide 25
The Currents in AA’, BB’, CC’ are 120 apart in time. Result is a 2-pole field distribution that rotates in space at a rotational speed s = e = 2f mechanical radians/sec
If the windings as in figure below, the result is a 4-pole field distribution (below right) that rotates at a rotational speed s = e/2 = f mechanical radians/sec
N
S
N
N
S
S
A
B’
C
A’
C
C’
C’
B
B
B’
A
A’

## Slide 26: How Magnetic Field B is Produced
Electrical frequency is elec. rads/s
B rotates in space at mech. rads/s
is called the synchronous speed. Or ns=120f/P in rpm
The greater no. of poles, the slower the synchronous speed
fe | e =2fe | P | s (rad/s) | ns (rpm)
50 | 314 | 2 | 314 | 3000
50 | 314 | 4 | 157 | 1500
50 | 314 | 6 | 105 | 1000
50 | 314 | 8 | 78 | 750
50 | 314 | 10 | 63 | 600

## Slide 27
1 rpm = 2 radians/minute = 2/60 radian/second (rads-1)
Therefore 1 rads-1 = 60/2  10 rpm
Stator windings of an Induction Machine (IM) can only be wound in one way. P is fixed for an individual machine. An IM can either be a 2-pole machine, or a 4-pole machine or ….etc

## Slide 28: Torque Production in an Induction Motor
B
S
B
v =Sl r
e = Blv
B
v =Sl r
I = Blv/Rbar
B goes round at S
Rotor goes round at r
Rotor sees B go round at sl = S - r
B goes past bars at v =sl r
r = radius of rotor
l = length of rotor bars
Emf (voltage) INDUCED
in bars is:
e = Blv = Blsl r
Hence currents flow in bars is:
I = Blv/Rbar
I = Blsl r/Rbar
I  sl
s : magnetic field speed
r : Rotor speed
sl : Slip speed

## Slide 29
B
B
I = Blv/Rbar
F=BIl
F
B
F
B “arrow” is where B is max.
Ir distribution is as above.
Maximum current is where max B is.
Induced current distribution goes round with B.
Rotor sees current pattern go round at sl = S - r
Force acts on current flowing in B
F= B I l
F is continuous since
B and I distribution go round together.
Force will act as above
(Force shown on 2 currents only)
T = Torque = Fr
T  B I l, I  sl
T  sl
Torque causes rotor to rotate at r
Steady state speed reached when T balances mechanical load (eg. friction etc)
If rotor catches up with B, then T must be zero since sl = S - r is zero

## Slide 30: Rotor Currents, Slip and Torque
B goes past rotor conductors at synchronous speed s
Rotor conductors see changing field (like changing flux in TF)
Hence currents induced in the rotor bars (like I induced in TF secondary)
Currents will react with B to give a torque
Rotor will rotate and tries to catch up with B
If catches up, r = s , now rotor sees stationary B (or flux). Hence T = 0
Bigger difference in s - r ( = slip ), greater rotor currents, greater T
In fact, T  slip. Let's plot Torque against rotor speed:

## Slide 31
All IM's have:
Trated: Rated continuous torque
(lf more, Ir will be too high, rotor will become too hot)
r rated: Rated speed of 4 pole motor e.g. 1460 rpm
Rated speed of 6 pole motor e.g. 940rpm
slip rated s - r rated in either rpm or mechanical rads-1
Normalised slip usually in % (should be small!)
As r goes from s to zero, s goes from 0 to 1
T
r
s
Trated
rated
slip
slip_rated
S=1
S=0

## Slide 32: Maximum Torque and Starting Torque
Complete rest of T-speed curve (just accept this)
Also plot Istator (written Is)
- as slip increase, Ir increases
- Ir sets up (rotating) field of its own to try and reduce main B
- Not allowed to do this! See TF operation!
- Additional Is flows to nullify field of Ir

## Slide 33
Can start IM by switching onto 3 mains (DOL start)
Pull out torque usually 2 to 3 x Trated
Tstart normally less than Tpull out
Is at start can be very large, often 5 to 8 x Is_rated
IM must accelerate quickly to point P so that large Is flows only for a short time
s
T
r
s
Trated
IStator
IStator
P
Load
Starting torque
Pull out torque

## Slide 34: Per-phase Equivalent Circuit
Look at one phase of IM. eg. Phase A
Let motor be connected to 50Hz mains, with no load.
In steady state r  s
No rotor currents
Is = Io , current to set up B called no-load current
VS
Is
Lo
Io

## Slide 35: Per-phase Equivalent Circuit
Now load up machine:
Slows down by slip and Ir starts to flow
An extra Is flows to cancel field of the rotor current, since B is determined by the applied voltage
Equivalent circuit like TF:
Vs
Im
Lo
Ir
lr
Rr
Ir'
Is
Ns : Nr

## Slide 36
Ns : Nr unknown (no rotor coils to compare stator coils with)
Rr is unknown
Ir is unknown (in rotor bars - never come out into outside world)
But Ir' is the extra stator current that flows under load
Since everything about real rotor is "unknown", makes sense to refer it to the stator side.
Passing the rotor parameters through the ideal TF we get:
Vs
Io
Lo
lr'
Rr' / s
Ir'
Is

## Slide 37
Note Rr becomes Rr /s (just accept this now). For more details see the handout on Induction motor equivalent circuit.
When s = 0 , Rr /s =  , Ir = 0
Unlike TF, Ir never seen. We will drop the ' from now on.
Ir used to denote extra stator current when IM is loaded.
There is one circuit for each phase. But Vs and Is etc… in Phases B and C will lag 120 and 240 behind Phase A.
For analysis, only necessary to consider one phase cct.
Machine may be connected in star or delta: see next slide

## Slide 38
It is Vs and Is that are used in the equivalent circuit
But IMs have a rated stator voltage and current – these are always VL and IL !
e.g. A  connected IM is rated at 415V, 25A.
Hence Vs_rated = 415V, Is_rated = 25/3
Vs
VL
Is
IL
Vs
VL
IL
Is

## Slide 39: Effect of Rotor Leakage Inductance
B
v =Sr
e = Blv
B
v =Sr
I  Blv/Rbar
Emf (voltage) INDUCED
in bars
e = Blv = Blsl r
This is same as before
Maximum e induced in bars where B is maximum.
But currents in bars no longer I = Blv/Rbar because rotor bars now exhibit inductance due to leakage lr
Currents will lag (in time) the induced voltage e.

## Slide 40
B

F
B
F
The effect is that the current distribution appears to lag the field.
The maximum current no longer occurs at the maximum B
The force F is now F = BIlcos
(Force shown on 2 currents only)
The torque is now T  BIl cos
It has been reduced.
  In practice, it is found that as the real bar currents increase, the leakage increases and  gets larger and larger. Eventually, this causes the torque to reduce.
  The effect explains why the torque-speed curve starts to bend away from a straight line and why there is a pull-out torque.

## Slide 41: Power Flows and Motor Torque
Can split the term into
Vs
Io
Lo
Xr =e lr
Rr(1-s)
s
Ir
Is
Rr
Pheat
Pmech
e = 2fe = 314
Power transferred across the air gap splits into two:
Pair gap = Power lost as heat in bars + Mechanical Power
Pair gap = Pheat + Pmech ie:

## Slide 42
Note the "3" because we have 3 phases
means the square of the rms (phasor) value
Pmech = Torque x angular rotor speed
Pmech = Tr
Now


## Slide 43
Hence:
And you see that the r terms cancel. It is convenient to replace s with the electrical frequency e . Remember that:
Ir is the extra stator current flowing when a load is applied (ie. the rotor slips). It is better to have the expression in terms of the applied stator voltage Vs.
From circuit diagram, we can calculate Ir in terms of Vs. We are in steady state AC, therefore we should use phasors:

## Slide 44
Vs
Ir
Xr =je lr
Rr / s
Original circuit:
Vs
Ir
Ir
Is
Vs
Vs
Rr
Xr =je lr
Where
and

## Slide 45
Hence:
and
This expression has only one variable – s!
Therefore plotting the expression against s: see next slide

## Slide 46
T
r
s
s
Tmax
By putting can show that Tmax occurs at
In operating region, neglect Xr

## Slide 47
and we see that T  s
For reference, Tstart obtained from putting s = 1 in Full
expression:

## Slide 48: Induction Motor Equivalent Circuit - Example
A 3-phase Cage Rotor Induction Motor with 2 pole-pairs is connected in delta and is fed from a 415V, 50Hz supply. The machine is mechanically loaded so that it runs at a slip of 2%. The parameters of the machine referred to the stator are: Rotor Resistance 0.2 and Rotor Leakage Inductance = 10mH. The stator resistance, stator leakage inductance and the iron losses may be neglected. Determine:
i. The speed of the rotating field in rpm. [1500rpm]
ii. The rotor speed in rpm.[1470rpm]
iii. The magnitude of rotor current per-phase referred to the stator. [39.6A]
iv. The total power input to the rotor. [47.045kW]
v. The power lost as heat in the rotor. [941W]
vi. The torque produced by the machine. [299Nm]

## Slide 49
EXERCISE: Slip A three-phase 415 V (line-to-line voltage), 50 Hz induction motor runs at 1478 rpm. Determine the number of poles, the slip and the frequency of the rotor current. SOLUTION: Because the synchronous speed must be slightly higher than the running speed and because at 50 Hz the only possibility is 1500 rpm.
The induced emf in the rotor is due to the slip speed, and therefore frotor = s x f = 0.015 x 50 Hz = 0.75 Hz

## Slide 50: Examples
A 4 pole machine on a 50 Hz supply is running at a speed of 1440 rpm what is the slip?
A 10 pole machine operates at a speed of 700 rpm at a slip of 0.0278 what is the supply frequency?
A 50 Hz 4 pole machine is operating at a speed of 1560 rpm what is the slip?
A 6 pole machine operating from a 50 Hz supply has a slip of 1.96, what is the mechanical speed?
(a) 60 rpm (b) 4% (c) -0.04 (d) none of the above
(a) 980.4 rpm (b) 960 rpm (c) -960 rpm (d) none of the above